## Slide 1: An Introduction to Next Generation Wireless Networks
Ioannis Pefkianakis
Hewlett Packard Labs
ioannis.pefkianakis@hpe.com

## Slide 2: Emerging Wireless
Call for transition to gigabit wireless
new apps require multi-Gbps speeds …
2011
2016
2021
2026
Source: Cisco VNI, 2016 - 2021
590 x GB
~20x
86.9 x GB
4.8 x GB
… generating huge volumes of data
Notes: VR/AR: Uncompressed streaming requires ~5 Gb/s speed with sub-10 ms latency
Self-driving car: Can locally generate up to 100 Gb/s
=============================
Source: Cisco VNI Mobile, 2016
http://www.cisco.com/c/en/us/solutions/collateral/service-provider/visual-networking-index-vni/mobile-white-paper-c11-520862.pdf
Traffic at 2015: 3.7 EB / month
Traffic at 2020: 30.6 EB month
Figures in parentheses refer to 2015, 2020 device share.
The “other portable devices” category includes readers, portable gaming consoles, and other portable devices with embedded cellular connectivity.
Wearables are included in the “M2M” category.
M2M connections (e.g., GPS systems in cars, asset tracking systems in shipping and manufacturing sectors, or medical applications making patient records and health status more readily available, et al.).
1 EB = 10006bytes = 1018bytes

## Slide 3: Roadmap
Background on wireless (Wi-Fi) networks
  From legacy to gigabit wireless
Multiple-Input, Multiple-Output (MIMO) gigabit wireless
Moving from low-frequency to millimeter-wave wireless

## Slide 4: IEEE 802.11 (Wi-Fi)
Standard for wireless local area networks (Wireless LANs) developed in 1990 by IEEE
Applications: enterprise, campus, home wireless network connectivity, cellular network data offloading
The 802.11 standard describes the MAC-layer and the PHY-layer
  MAC-layer: Access control, reliable delivery, security
  PHY-layer: modulation, coding, operation frequency, antenna technology etc.
Notes: The aim of digital modulation is to transfer a digital bit stream over an analog bandpass channel,
The physical layer defines the means of transmitting raw bits rather than logical data packets over a physical data link connecting network nodes.

## Slide 5: Wi-Fi Network Setup
Infrastructure W-Fi mode:
  A Basic Service Set (BSS) (or cell) contains wireless devices and an Access Point (AP) ( or base station)
  Multiple BSSs form a distribution system (DS)
Ad-hoc Wi-Fi mode:
  Wireless devices dynamically form a network without APs

## Slide 6: Physical (PHY) Layer
Wi-Fi operates on 2.4 GHz and 5-GHz bands
Typically it uses orthogonal frequency division multiplexing (OFDM)
  Also called multicarrier modulation
OFDM transmits a few bits on each subchannel/subcarrier
  Similar to FDM but all subchannels dedicated to single source
PHY transmission rate or wireless speed depends mainly on: a) modulation, b) coding rate, c) channel bandwidth, d) antennas (MIMO)
802.11a data rates: 6, 9, 12, 18, 24, 36, 48, and 54 Mbps
  Up to 52 subcarriers modulated using BPSK, QPSK, 16-QAM, or 64-QAM
Notes: The physical layer defines the means of transmitting raw bits rather than logical data packets over a physical data link connecting network nodes.

## Slide 7: Medium Access Control
802.11 supports CSMA/CA for controlling access to the wireless channel
802.11 CSMA: sender
If sense channel idle for DIFS (Distributed Inter Frame Space) then transmit entire frame (no collision detection)
If sense channel busy then binary backoff
802.11 CSMA: receiver
If received OK return ACK after SIFS --Short IFS (ACK is needed due to hidden terminal problem)
Others: RTS/CTS and NAV are used to further avoid collisions

## Slide 8: From Legacy to Gigabit Wireless
Space (MIMO): Multiple antennas (Nt ,Nr)
Frequency
Frequency-agile communication
New spectrum (mmWave communication)
Time
New medium access control protocols
Capacity = B  log2(1+SNR)
Capacity = min{Nt, Nr}  B  log2(1+SNR)

## Slide 9: Wi-Fi Evolution
What is new in 802.11ac/ax?
Legacy 802.11a/b/g:
Speeds up to 54 Mbps
1999-2003
2009
HT 802.11n:
Speeds up to 600 Mbps
2013
VHT 802.11ac:
Speeds > 6 Gbps
2019
HE 802.11ax:
Speeds > 9 Gbps
Channel bandwidth | Tx/Rx antennas (MIMO) | Modulation & coding | Data rate
20 MHz | 1x1 | 64-QAM, 3/4 | 54 Mbps
40 MHz | 4x4 | 64-QAM, 5/6 | 600 Mbps
160MHz | 8-ant AP / 4, 2-ant STAs (MU-MIMO) | 256-QAM, 5/6 | 6.9 Gbps
802.11a
802.11n
802.11ac
Notes: WiFi has been changing a lot the last 15 years to accommodate the huge data volumes generated by wireless devices
802.11b has a maximum raw data rate of 11 Mbit/s and uses the same CSMA/CA media access method defined in the original standard. Due to the CSMA/CA protocol overhead, in practice the maximum 802.11b throughput that an application can achieve is about 5.9 Mbit/s using TCP and 7.1 Mbit/s using UDP.

## Slide 10: Multiple-Input Multiple-Output (MIMO)
MIMO uses multiple antennas at the sender (Nt) and receiver (Nr) to increase speed from megabit (54Mbps in legacy Wi-Fi) to gigabit (6.9 Gbps in VHT Wi-Fi)
Spatial diversity transmits the same stream from each antenna
  More reliable transmission
  Packer error rate: Pe = 1/SNRNt⋅Nr

## Slide 11: Multiple-Input Multiple-Output (MIMO)
MIMO uses multiple antennas at the sender (Nt) and receiver (Nr) to increase speed from megabit (54Mbps in legacy Wi-Fi) to gigabit (6.9 Gbps in VHT Wi-Fi)
Spatial multiplexing (SM) transmits multiple independent streams simultaneously
  Increased data rate
  Capacity: C = min{Nt, Nr} ⋅W⋅log2(1+SNR)

## Slide 12: From MIMO to Multi-User MIMO
MIMO: Multiple antennas at the sender and receiver
  SU-MIMO: An Access Point (AP) transmits multiple data streams to one user at a time
  MU-MIMO: An AP transmits multiple data streams concurrently to different users
    Beamforming allows an AP to steer the RF energy in a specific direction, towards a user
SU-MIMO speed is limited by the #antennas at the user!
Stream 1
Stream 2
Single-User MIMO
Stream 1
Stream 2
Stream 3
Stream 4
Multi-User MIMO
Notes: Diversity: Packer error rate: Pe = 1/SNRNtNr
Spatial Multiplexing: Capacity: C = min{Nt, Nr} Wlog2(1+SNR)
WLAN: 11n is 600 Mbps, 11ac in 6.9 Gbps, 11ax 9.6 Gbps
LTE-A: LTE-Advanced standard (3GPP Release 11) supports 8×8 MIMO in the downlink and 4×4 MIMO in the uplink. http://www.unwiredinsight.com/2013/lte-mimo

## Slide 13: Beamforming
How does beamforming work?
Training frame
Compressed Channel report V
Training frame
Compressed channel report V
Training frame
Singular Value Decomposition
Beamed data
Beamed data
The AP precodes the transmission data x as: u=V∙x
Upon receiving the precoded data, each user k
applies the matrix U to extract its own data
(treating others’ data as interference)
Ideally Vk and Vj must be orthogonal
Notes: Note that in Eq. (4), D and V are different random variables and can be considered uncorrelated.
Ideally we want the precoding martix Vk to be orthogonal to all other user channels Vi

## Slide 14: Key Functions For MU-MIMO Wi-Fi
Wireless standards allow the use of multiple transmission rates
  802.11ac rates from 6Mbps up to 6.9 Gbps (> 600 rate options)
Rate Adaptation (RA) adjusts the speed based on the channel condition
Sender
Receiver
Receiver
Strong signal
Weak signal
6Mbps: Loss=0% ® Speed = 6Mbps
600Mbps: Loss=0% ® Speed = 600Mbps
6Mbps: Loss=0% ® Speed = 6Mbps
600Mbps: Loss=100% ® Speed = 0Mbps
Rate Adaptation: The key to utilize wireless channel capacity

## Slide 15: Key Functions For MU-MIMO Wi-Fi
User selection determines which users to be served concurrently
  User selection needs to identify MU-MIMO user groups with uncorrelated channels
×
wrong grouping → correlated channels →
inter-user interference → poor performance
433 Mbps
(strong signal)
130 Mbps
(weak signal)
User and rate selection are fundamental algorithms for MU-MIMO performance

## Slide 16: Key Functions For MU-MIMO Wi-Fi
In high-density Wi-Fi deployments each client has multiple APs in its range
?
AP Selection algorithms should appropriately assign devices to APs to improve performance
Notes: High density Wi-Fi is a design strategy for large deployments to provide pervasive connectivity with 10 or more access points in the same space and more than 40 devices connected to any access point.

## Slide 17: Algorithms on Commodity Networks
MU-MIMO user and rate selection are trial-and-error based
Packet error rate increases
300 Mbps?
260 Mbps?
230 Mbps?
170 Mbps?
Nope!
Nope!
Nope!
Nope!
Okay!
50 Mbps?
High convergence time and poor
performance for legacy algorithms
Notes: Fig. 5(c) shows distribution of users’ PER. Whereas PER is negligible in SU-MIMO, it can exceed 60% for Legacy-US. Interestingly, for certain settings

## Slide 18: Algorithms on Commodity Networks
C1
C2
C4
RSSI: -47
RSSI: -48
RSSI: -46
C3
RSSI: -46
RSSI: -50
?
X
Legacy AP selection
ThroughputC3 = 9 Mbps
MU-MIMO-Aware AP selection
ThroughputC3 = 145 Mbps
Legacy designs limit grouping opportunities by assigning
devices with correlated channels to the same AP
AP1
AP2
Notes: C3 achieves ~16 times more throughput at AP1

## Slide 19: How to Optimize Next-Generation MIMO Wi-Fi?

## Slide 20: Roadmap
Background on wireless (Wi-Fi) networks
  From legacy to gigabit wireless
Multiple-Input, Multiple-Output (MIMO) gigabit wireless
Moving from low-frequency to millimeter-wave wireless
Limitation: Wireless technologies (e.g., Wi-Fi) operate on limited, highly-congested spectrum

## Slide 21: New Opportunity at Very-High-Frequency Bands
Today’s LTE and Wi-Fi operate here
Large unlicensed spectrum at millimeter-wave
≈
0 GHz 10 GHz 20 GHz 30 GHz 40 GHz 50 GHz 60 GHz 70 GHz 80 GHz 90 GHz 300 GHz
Notes: Extremely high frequency (EHF) is the International Telecommunications Union (ITU) designation for the band of radio frequencies in the electromagnetic spectrum from 30 to 300 gigahertz.
The 71-76, 81-86 and 92–95 GHz bands are also used for point-to-point high-bandwidth communication links, but require FCC approval
U.S. Federal Communications Commission (FCC) approved the spectrum for 5G, including the 28 Gigahertz, 37 GHz and 39 GHz bands
mmWave bands:
57 GHz to 64 GHz unlicensed.
Seven gigahertz in total 28 GHz/38 GHz licensed but underutilized.
Three gigahertz in total 71 GHz/81 GHz/92 GHz Light-licensed band: 12.9 gigahertz in total.
https://www.rcrwireless.com/20160815/fundamentals/mmwave-5g-tag31-tag99
802.11ad channels:
4 channels are defined with 2.26 GHz bandwidth. In the US 3 are used. In Europe all 4 channels are available
https://cdn.rohde-schwarz.com/pws/dl_downloads/dl_application/application_notes/1ma220/1MA220_2e_WLAN_11ad_WP.pdf
Why did you show 24 GHz in the plot with yellow?
“Last October, the FCC proposed new rules for wireless broadband in wireless frequencies above 24 GHz. ”
So 24 GHz is like the frontier: https://www.rcrwireless.com/20160815/fundamentals/mmwave-5g-tag31-tag99
24 GHz is unlicensed band. Its wavelength is just above 10 mm 12.5 mm
The 24GHz band (22–29GHz) band and 77GHz band (76–77GHz) are currently assigned to automotive radar.

## Slide 22: New Opportunity at Very-High-Frequency Bands
Today’s LTE and Wi-Fi operate here
Large unlicensed spectrum at millimeter-wave
≈
0 GHz 10 GHz 20 GHz 30 GHz 40 GHz 50 GHz 60 GHz 70 GHz 80 GHz 90 GHz 300 GHz
Millimeter-wave spectrum
…
Notes: Compare that…with how much we have at mmWave. Between, 30 to 300 GHz, about 1000 times wider free spectrum

## Slide 23: New Opportunity at Very-High-Frequency Bands
Today’s LTE and Wi-Fi operate here
Large unlicensed spectrum at millimeter-wave
≈
0 GHz 10 GHz 20 GHz 30 GHz 40 GHz 50 GHz 60 GHz 70 GHz 80 GHz 90 GHz 300 GHz
Millimeter-wave spectrum
…
Off-the-shelf (IEEE 802.11ad) devices offer up to 7 Gbps of wireless bit-rate!
2 GHz slice
Notes: And using a tiny 2 GHz slice, today’s off-the-shelf devices can already go up to 7 Gbps wireless bit rate
27 times higher bandwidth than wifi (2.16 GHz/80 MHz)

## Slide 24: Challenges for 60 GHz Communication
Attenuation: 60 GHz signal propagation loss is huge compared to Wi-Fi
  additional 22 dB attenuation compared to 5GHz Wi-Fi
Directionality: narrow beams bring new challenges in link establishment and maintenance
4x8 phased-array
17 mm
8 mm
Notes: At a typical IEEE 802.11ad range of 10 m, additional attenuation of 22 dB compared to the 5 GHz band is predicted by the Friis transmission equation: http://ieeexplore.ieee.org/abstract/document/6979964/

## Slide 25: Challenges: 60 GHz Slow Convergence
Naïve search for the best beam and rate in the 60 GHz large configuration space leads to huge convergence times
Identifying the best beam and MCS setting takes up to 910 ms!

## Slide 26: Challenges: 60 GHz Link Blockage
Link throughput > 2 Gbps
60 GHz signal amplitude
Even aligning the beams does not guarantee link connectivity
Notes: Can completely kill link connection
So, here is an example. While today’s device can achieve more than 2 Gbps throughput,… a single blockage like tip of your finger will kill the link connection. So, imagine when this antenna will go to mobile phones
THIS…is a serious challenge…
And it can not solved by placing ten, hundred or even thousands of access points, mirrors, reflectors in the room
What can we do? …

## Slide 27: 60 GHz vs. Wi-Fi
Experimental Platform
Qualcomm dual band (5 GHz WiFi & 60 GHz) Access Point, Intrinsyc dual band tablet
32 phased-array antennas at 60 GHz, 4 MU-MIMO antennas at 5 GHz WiFi
Supports up to 4.62 Gbps PHY bit-rate at 60 GHz
32 phased-array antennas: Area ~ 2.5cmX1.3cm
60 GHz + WiFi Access Point
60 GHz + WiFi tablet
Notes: The Access Point is a tri-band and supports both the traditional WiFi and new 60 GHz interface. It packs with 32 phased-array antennas in a small area of 2.5x1.3 cm^2. The client device is also tri-band capable device having same number of antennas. The Access Point support up 4.62 Gbps bit-rate

## Slide 28: 60 GHz vs. Wi-Fi
Application throughput comparison across 25 static locations around the lab
AP on table
AP on tripod
~9 ft.

## Slide 29: 60 GHz vs. Wi-Fi
Application throughput comparison across 25 static locations around the lab
40%
60 GHz is better
WiFi is better
Notes: So, we place the Access Point in one of the cubicle in the 2nd floor lab and place client devices around 20 different static locations in 15x15 m^2 area. At each of the locations, we measured applications throughput from both the 60 GHz, which is also known as WiGig, and the traditional WiFi. Here is how the distribution of throughput differences between the two interfaces look like. Around 25% of such locations, 60 GHz performed really well, and it throughput can be around 1.5~1.9 Gbps, close to more than 1 Gbps higher than the WiFi links. While, rest of the 75% locations not so well. In fact, many locations we could not establish the link connection at all with 60 GHz interface

## Slide 30: 60 GHz vs. Wi-Fi
Application throughput comparison across 25 static locations around the lab
60 GHz is better
WiFi is better
72%
Notes: So, we place the Access Point in one of the cubicle in the 2nd floor lab and place client devices around 20 different static locations in 15x15 m^2 area. At each of the locations, we measured applications throughput from both the 60 GHz, which is also known as WiGig, and the traditional WiFi. Here is how the distribution of throughput differences between the two interfaces look like. Around 25% of such locations, 60 GHz performed really well, and it throughput can be around 1.5~1.9 Gbps, close to more than 1 Gbps higher than the WiFi links. While, rest of the 75% locations not so well. In fact, many locations we could not establish the link connection at all with 60 GHz interface

## Slide 31: Designing Ubiquitous Gbps Wireless Access Network
UbiG: guaranteed-latency, ubiquitous, robust mmWave connectivity, using low-cost, off-the-shelf hardware
Predictive Link Adaptation
with constant probing overhead
Ranking-Based AP Switching
for Gbps connectivity under mobility
Multiband-Assisted mmWave
proactive FST from blocked 60 GHz links to Wi-Fi
Notes: Scalable beam alignment: UbiG seeks to align the beam between the mmWave devices, at a latency that is independent of the size of the phased-arrays.
(2) Ubiquitous Gbps connectivity: UbiG seeks to maintain Gbps connectivity even under blockage or mobility. Ultra-dense AP
deployment and fast AP switching are required to sustain Gbps connectivity
(3) Low hardware cost: UbiG needs to be implementable on off-the-shelf standard-compatible mmWave
hardware, which may not provide coherent PHY layer information, or only allows for coarse-grained phase control
over the phased-array antenna elements.

## Slide 32: Demo
Notes: Our experiments
show that in 82% of the settings, the SNR loss from
UbiG’s O(K) beam alignment is less than 1.5 dB (in
comparison to the ground-truth), which enables nearoptimal
beam (and MCS) selection. Under simulated
settings, the solution scales well even for large phasedarrays
with 1024 beams. The average SNR loss remains
less than 1 dB under medium to high SNR conditions.

## Slide 33: Summary
MIMO and millimeter-wave are key technologies for the next generation wireless
Time to rethink protocols over the new gigabit wireless networks
  Key requirements:
    new metrics
    multi-band cooperation
    new implementation architectures

## Slide 34: Thank you
ioannis.pefkianakis@hpe.com