## Slide 1: On the (Glottal) Inverse Filtering of Speech Signals
An introduction
CS578-Digital speech signal processing
Invited lecture

## Slide 2: On the (Glottal) Inverse Filtering of Speech Signals
Introduction
Inverse Filtering Techniques
Conclusions

## Slide 3: Introduction

## Slide 4: On the (Glottal) Inverse Filtering of Speech Signals
The human speech production system is a complicated system
From an engineering point of view, it can be roughly divided into three parts [1]
  The vocal folds, which is the source of the system
  The vocal tract filter, which is the path from the vocal folds to the lips
  The lip radiation, which is the final bound before system output

## Slide 5: On the (Glottal) Inverse Filtering of Speech Signals
Based on this simplification, voiced speech can be modeled as a linear filtering operation:
where denotes convolution and
  is the glottal airflow velocity waveform
  is the vocal tract filter
  is the lip radiation filter

## Slide 6: On the (Glottal) Inverse Filtering of Speech Signals

## Slide 7: On the (Glottal) Inverse Filtering of Speech Signals
What is Glottal Inverse Filtering (GIF)?
  GIF refers to techniques for obtaining the source of voiced speech, the glottal airflow velocity waveform, from voiced speech itself [10]
  How does this signal look like?
  Open phase: air flows through the glottis
  Return phase: vocal folds are snapping shut
  Closed phase: glottis is shut and airflow velocity is zero

## Slide 8: On the (Glottal) Inverse Filtering of Speech Signals
While radiation occurs after the vocal tract filter, we often combine and into a single expression
  This applies the radiation effect to the glottal source before it enters the vocal tract
  Effect of differentiation on the source
The resulting signal is the so-called glottal flow derivative
Very commonly used in literature

## Slide 9: On the (Glottal) Inverse Filtering of Speech Signals
Why bother?
  Basic research of speech production
  Applications to speech analysis, synthesis, and modification
  Environmental voice care
  Voice pathology detection
  Analysis of the emotional content of speech
  Voice source modeling for TTS

## Slide 10: On the (Glottal) Inverse Filtering of Speech Signals
Basic idea:
  Form a computational model for the vocal tract filter,
  Cancel its effect from the speech waveform by filtering the speech signal through the inverse of the model,

## Slide 11: On the (Glottal) Inverse Filtering of Speech Signals
Problem:
  The actual glottal flow waveform IS NOT AVAILABLE!
  …at least in a non-invasive manner [18]
Approaches:
  “Visual” inspection of the resulting glottal flow waveform
  Use of synthetic speech signal produced by a known artificial excitation
  Compare the results of different GIF algorithms
None of the previous approaches is truly objective

## Slide 12: On the (Glottal) Inverse Filtering of Speech Signals
One solution is to build a physical model of the speech production mechanism
  Generate waveforms from this model
Time-varying waveforms are simulated
Such waveforms are expected to provide a more firm and realistic test of GIF methods
Both the speech output and the source are available
A well known dataset of such signals is described in [2,6]

## Slide 13: On the (Glottal) Inverse Filtering of Speech Signals

## Slide 14: On the (Glottal) Inverse Filtering of Speech Signals
The model has a parametrized input such as
  Lung pressure
  Prephonatory glottal half-width (adduction)
  Vocal fold length and thickness
  Activation levels of the cricothyroid and thyroarytenoid muscles

## Slide 15: On the (Glottal) Inverse Filtering of Speech Signals

## Slide 16: GIF techniques

## Slide 17: On the (Glottal) Inverse Filtering of Speech Signals
Since we already know about Linear Prediction (LP), we will discuss GIF methods based only on that
You already know two methods for estimating LP coefficients
  Autocorrelation method: zero samples outside prediction error interval –minimize MSE everywhere
  Covariance method: non-zero samples outside prediction error interval – minimize MSE inside prediction error interval

## Slide 18: On the (Glottal) Inverse Filtering of Speech Signals
LP is used to produce all-pole models of the vocal tract filter
where is the filter order and are the LP coefficients
In general, LP minimizes the MSE over a region R
where

## Slide 19: On the (Glottal) Inverse Filtering of Speech Signals
How can we find the source excitation through LP analysis?
If we consider speech as an AR process
then minimization of the MSE leads to
Thus, the prediction error (or residual) can be thought of an estimation of the source excitation
But how are glottal source and residual related?

## Slide 20: On the (Glottal) Inverse Filtering of Speech Signals
Speech frame
Residual (prediction error)

## Slide 21: On the (Glottal) Inverse Filtering of Speech Signals
But how are glottal source and residual related?
As you’ve seen, the two signals do not quite match
The reason is that the Z transform of speech is a combined transfer function
can be further decomposed as an impulse sequence passed through a glottal filter: , where is the impulse sequence
Thus contains
Zeros from the glottal source and lip radiation
Poles from the glottal filter and the vocal tract filter

## Slide 22: On the (Glottal) Inverse Filtering of Speech Signals
LP analysis provides an overall transfer function where all these contributions are combined!
  …not to mention that we’re using an all-pole method for a pole-zero signal…
So what we are cancelling via simple LP-based GIF is this overall estimation
  …resulting into something that looks like a series of impulses!
So how can we work this out?
Identify instants where there is no interaction between the source and the filter!

## Slide 23: On the (Glottal) Inverse Filtering of Speech Signals
Closed-phase analysis
Identify regions where the vocal folds are closed
  No contribution from , the speech signal should contain vocal tract and radiation factors
  can be modeled as a differentiator (single-zero FIR filter), so it can be cancelled by a simple integrator
Vocal tract estimation in the closed phase region leads to a more precise result
Estimation in the closed phase  cancelling vocal tract via GIF over the whole pitch period
Use of covariance-based LP on the closed-phase [9]

## Slide 24: On the (Glottal) Inverse Filtering of Speech Signals
Closed-phase analysis

## Slide 25: On the (Glottal) Inverse Filtering of Speech Signals
However, standard closed-phase covariance LP suffers from certain shortcomings
Short closed phase duration (especially for high pitched speakers)
  Too few samples to obtain a good estimation
Sensitivity to the exact position of the covariance frame
  Small variation from the exact closed phase interval produces artifacts
Vocal tract filter instability
  Covariance-based LP does not guarantee a stable filter
  Inverse filter might not be minimum phase

## Slide 26: On the (Glottal) Inverse Filtering of Speech Signals
Frame position sensitivity

## Slide 27: On the (Glottal) Inverse Filtering of Speech Signals
The effect of an inverse filter root which is located on the positive real axis has the properties of a first order differentiator, when the root approaches the unit circle
A similar effect is also produced by a pair of complex conjugate roots at low frequencies
This distortion is more apparent at the time instants where the glottal flow changes more rapidly, that is, near glottal closure
The presence of such roots are in contrast to the source-filter suggested theory
The removal of such roots results in less dependency on the covariance frame location

## Slide 28: On the (Glottal) Inverse Filtering of Speech Signals
Non-minimum phase inverse filter

## Slide 29: On the (Glottal) Inverse Filtering of Speech Signals
The inverse filter might not be minimum phase
As we know from basic DSP, it can become minimum phase by replacing each zero by its mirror image partner
That leaves the magnitude spectrum unchanged
The phase characteristics change, though

## Slide 30: On the (Glottal) Inverse Filtering of Speech Signals
Constrained Covariance-based Closed-Phase LP [3]
Idea: modification of the conventional CP covariance analysis in order to provide more realistic root locations, in the acoustic sense
How?
  Not allow mean square error to locate the roots freely on the z-plane
  Impose mathematical restrictions in a form of concise mathematical equations
  DC-constraint

## Slide 31: On the (Glottal) Inverse Filtering of Speech Signals
Constrained Covariance-based Closed-Phase LP [3]
DC-constraint:
Why?
  Magnitude response of voiced sounds approaches unity at zero frequency [1]
  A short and misplaced covariance frame might lead to a response with higher gain at DC than at formants
With such a constraint, one might expect a better match of the magnitude response to the source-filter theory

## Slide 32: On the (Glottal) Inverse Filtering of Speech Signals
Constrained Covariance-based Closed-Phase LP [3]
Constrained convex minimization problem
Minimize subject to
Solution:

## Slide 33: On the (Glottal) Inverse Filtering of Speech Signals
Still, the computational load of covariance-based LP along with its shortcomings (cases of very small CP, frame dependent, CP identification) might make the method not appropriate
Idea: use autocorrelation method with “enhancements”
  Fast & stable
  Not optimal but good enough
  Try to introduce “enhancements”
  Try to approach performance of CP analysis without detecting CP

## Slide 34: On the (Glottal) Inverse Filtering of Speech Signals
Iterative Adaptive Inverse Filtering [4]
An iterative method for obtaining the glottal source
Motivation:
  A priori knowledge of the overall shape of the vocal tract
  Cancel the tilting effect of the glottal source
  Estimate vocal tract filter

## Slide 35: On the (Glottal) Inverse Filtering of Speech Signals
Iterative Adaptive Inverse Filtering [4]
First iteration
1. LPC of order 1 to model the effect of the glottal source on the speech spectrum
2. Cancel 1.
3.LPC of high order to model the vocal tract
4&5. Cancel vocal tract and lip radiation

## Slide 36: On the (Glottal) Inverse Filtering of Speech Signals
Iterative Adaptive Inverse Filtering [4]
Second iteration
6. LPC of order 2-4 to more accurately model the effect of the glottal source on the speech spectrum
7. Cancel 6.
8.LPC of high order to model the vocal tract
9&10. Cancel vocal tract and lip radiation

## Slide 37: On the (Glottal) Inverse Filtering of Speech Signals
Stabilized Weighted Linear Prediction [5,7]
An all-pole method based on Weighted Linear Prediction (WLP)
Idea: use standard autocorrelation method but give more weight to some samples of the autocorrelation matrix compared to others
How to give more weight?

## Slide 38: On the (Glottal) Inverse Filtering of Speech Signals
Stabilized Weighted Linear Prediction
Compute the short time energy (STE) of the signal
High energy samples fall in the closed phase region!

## Slide 39: On the (Glottal) Inverse Filtering of Speech Signals
Stabilized Weighted Linear Prediction
STE function emphasizes the speech samples of large amplitude, which typically occur during the closed phase interval
By emphasizing on these samples that occur during the glottal closed phase, it is likely to yield more robust acoustical cues for the formants
The method depends on a parameter , the energy window length
A high value of increases the sharpness of the resonances of the spectrum, whereas a low value of M increases the smoothness of the spectrum

## Slide 40: On the (Glottal) Inverse Filtering of Speech Signals
Stabilized Weighted Linear Prediction
STE:
Prediction error energy:
where

## Slide 41: On the (Glottal) Inverse Filtering of Speech Signals
Stabilized Weighted Linear Prediction
Constrained minimization problem (again )
Minimize subject to , where
It can be shown that a satisfies the linear equation
where is the error energy
Stability is ensured by a specific algorithm

## Slide 42: On the (Glottal) Inverse Filtering of Speech Signals
Results

## Slide 43: On the (Glottal) Inverse Filtering of Speech Signals
Results

## Slide 44: On the (Glottal) Inverse Filtering of Speech Signals
Performance metric
: original glottal source
: error between original and synthetic
: standard dev. of
The bigger the better!
Signal to Reconstruction Error Ratio

## Slide 45: On the (Glottal) Inverse Filtering of Speech Signals
Performance metric
: original glottal source spectrum
: synthetic glottal source spectrum
is the difference between the first two glottal source harmonics
This metric is an indication of the spectral tilt
The smaller the better!

## Slide 46: Conclusions

## Slide 47: On the (Glottal) Inverse Filtering of Speech Signals
GIF has been around for more than five decades
Attractive analysis method
  Non-invasive
  Using only speech signal
  Mostly automatic
  Applications in many speech technologies
  Still improving! (QCP Analysis [16])
Software: OPENGlot, Aparat, etc

## Slide 48: On the (Glottal) Inverse Filtering of Speech Signals
GIF has been around for more than five decades
Shortcomings
  Recording should be made with caution
    Introducing non-linearities that distort GIF result
  “Ground truth” is very rarely available
    Synthetic speech or physiologically modeled data is used
  Unreliable analysis of certain voice types [11,12]
    High-pitch speech, low F1, vulnerability of best method (closed-phase CP)
  Based on all-pole methods  speech is pole-zero (nasal sounds)
  Fixed filter coefficients over successive periods

## Slide 49: References
[1] Fant G., Acoustic Theory of Speech Production (Mouton, The Hague).
[2] Story, B. and Titze, I. Voice simulation with a body-cover model of the vocal folds,” J. Acoust. Soc. Am., 97, 1249–1260, 1995.
[3] Alku, P., Magi, C., Santeri, Y., Backstrom, T., Story, B., Closed phase covariance analysis on constrained linear prediction for glottal inverse filtering, Journal of Acoustical Society of America, 125(5):3289-3305, 2009.
[4] Alku, P., Glottal wave analysis with Pitch Synchronous Iterative Adaptive Inverse Filtering. Speech Communication, 11(2-3), 109–118, 1992.
[5] Magi, C. , Pohjalainen, J., Backstrom, T., Alku, P., Stabilised Weighted Linear Prediction, Speech Communication, 51:401-411, 2009.
[6] Alku P., Story B., Airas M., Estimation of the voice source from speech pressure signals: Evaluation of an inverse filtering technique using physical modelling of voice production, Folia Phoniatr. Logo. 58(1): 102–113, 2006.

## Slide 50: References
[7] Kafentzis, G., Stylianou, Y. and Alku, P.,International Conference on Acoustics, Speech, and Signal Processing, Prague, Czech Republic, May 22-27, 2011. p. 5408-5411, 2011.
[8] Airaksinen, M., Raitio, T., Story, B., & Alku, P., Quasi Closed Phase Glottal Inverse Filtering Analysis With Weighted Linear Prediction. IEEE/ACM Transactions on Audio, Speech, and Language Processing, 22(3), 596-607, 2014.
[9] M. Plumpe, T. Quatieri, and D. Reynolds, Modeling of the glottal flow derivative waveform with application to speaker identification, IEEE Transactions on Speech and Audio Processing, 7:569-586, 1999.
[10] Wong D., Markel J., Gray A., Least squares glottal inverse filtering from the acoustic speech waveform, IEEE Trans. Acoust. Speech Signal Process. 27: 350–355, 1979.

## Slide 51: Other references
[11] Childers D., Ahn C., Modeling the glottal volume-velocity waveform for three voice types, J. Acoust. Soc. Am. 97(1): 505–519, 1995.
[12] Childers D., Lee C., Vocal quality factors: Analysis, synthesis, and perception. J. Acoust. Soc. Am. 90(5): 2394–2410, 1991.
[13] Milenkovic P., Glottal inverse filtering by joint estimation of an AR system with a linear input model, IEEE Trans. Acoust. Speech Signal Process. 34(1): 28–42, 1986.
[14] Raitio T., Suni A., Yamagishi Y., Pulakka H., Nurminen J., Vainio M., Alku P., HMM-based speech synthesis utilizing glottal inverse filtering, IEEE Trans. Audio Speech Lang. Process. 19(1): 153– 165, 2011.
[15] Shiga Y., King S., Estimation of voice source and vocal tract characteristics based on multi-frame analysis. CD Proc. Eurospeech, 1749–1752, 2003.

## Slide 52: Other references
[16] J. Pohjalainen, R. Saeidi, T. Kinnunen, and P. Alku, Extended weighted linear prediction (XLP) analysis of speech and its application to speaker verification in adverse conditions, in Proc. Interspeech, 2010, pp. 1477–1480.
[17] T. Drugman, B. Bozkurt, and T. Dutoit, A comparative study of glottal source estimation techniques, Comp. Speech & Lang., vol. 26, no. 1, pp. 20–34, 2012.
[18] Kitzing, P., & Löfqvist, A., Subglottal and oral air pressures during phonation—preliminary investigation using a miniature transducer system. Medical & Biological Engineering, 13(5), 644–648, 1975.